## Slide 1
CHAPTER 1
Smart Sensor Design
Fundamentals, Design Techniques, and Case Studies
EEE703708 · Smart Sensor Systems
Based on: Meijer, Pertijs & Makinwa — Smart Sensor Systems

## Slide 2
1 / 6
Sensors Are Everywhere
🚗 Cars
Position sensors
MEMS accelerometers
Gyroscopes
Tire pressure
Proximity / parking
🏠 Homes
Thermostats
Motion sensing
Gas / smoke flow
Door/window contacts
Water leak detection
📱 Mobile Phones
Touch + image sensors
MEMS microphones
Inertial sensing
E-compass
GPS + environment
Sensors transformed everyday devices — cars, homes, phones.

## Slide 3
2 / 6
Why Silicon?
Low Cost
Mass-producible by mature semiconductor industry
Integration
Sensor + interface circuitry in one substrate/package
Material Control
High-purity, tunable physical properties
Trade-off
Not always best raw performance; wins on cost + size + system integration
Silicon's value proposition: cost + size + integration.

## Slide 4
3 / 6
Silicon Transduction Mechanisms
MEASURAND | EFFECT | PRINCIPLE
Magnetic field | Hall effect | Transverse voltage in current-carrying plate
Temperature difference | Seebeck effect | Thermopile junction voltage
Mechanical strain | Piezoresistive | Resistance change under stress
Light | Photoelectric | Photodiode / phototransistor array
Humidity / gas | Indirect | Polymer dielectric / metal-oxide resistance
Many sensors convert physical effects into tiny electrical signals.

## Slide 5
4 / 6
What Is a Smart Sensor?
Definition
System-in-package combining a sensor with dedicated interface electronics
Close Coupling
Electronics near sensor reduce interference and transmission losses
Examples
Single-chip: temperature, image, Hall
Two-chip: MEMS accel, gyro, mic
Added Functions
Signal conditioning
Standardized output
Self-test + self-calibration
Sensor fusion
Smart sensor = sensing element + nearby intelligence.

## Slide 6
5 / 6
Smart Sensor Design = System Design
Optimize Operation
Run the sensing element in its best physical/electrical mode
Compensate Errors
Correct cross-sensitivity, temperature effects, package stress
Use Feedback
Improve linearity, bandwidth, dynamic range
Package Correctly
Expose sensor to measurand while protecting the device
Performance comes from optimizing sensor + electronics + packaging together.

## Slide 7
6 / 6
Interface Electronics: The Challenge
Weak Signals
Thermopiles, Hall plates, strain gauges often produce microvolt-level outputs
Transparent Interface
Circuit noise, offset, drift must not dominate sensor performance
Early Digitization
Convert to digital early, then filter / linearize / compensate in DSP
The interface must reveal the sensor — not become the sensor limit.

## Slide 8
2 / 6
The DC Signal Problem
Sensor Reality
Many measurands include DC or low-frequency components
CMOS Limits
Drift, 1/f noise, mismatch, charge injection, leakage
Precision Strategy
Dynamic error correction trades speed/bandwidth for accuracy
Two Families
Sample-and-correct
Modulate-and-filter
Low-frequency precision is hard; dynamic techniques make it practical.

## Slide 9
2 / 6
Auto-Zeroing: Sample-and-Correct
1. Sample
Short input; measure offset
→
2. Store
Offset-canceling integrator stores correction
→
3. Amplify
Apply correction during normal sensing
→
4. Ping-Pong
Two amps alternate to avoid downtime
Auto-zeroing cancels offset + 1/f noise, but reduces availability unless ping-ponged.

## Slide 10
2 / 6
Chopping: Modulate-and-Filter
1. Modulate
Move sensor signal to chopping frequency
→
2. Amplify
Offset + 1/f noise stay near DC
→
3. Demodulate
Signal returns to baseband
→
4. Filter
Remove shifted error terms
Chopping achieves excellent low-frequency precision; filter limits bandwidth.

## Slide 11
2 / 6
Sigma-Delta Modulation
Input
Low-bandwidth analog sensor signal
→
Loop
Filter + ADC + DAC feedback
→
Noise Shape
Quantization noise pushed out-of-band
→
Digital LPF
Remove out-of-band noise → high resolution
Can reach 20+ bit resolution in narrow bandwidths

## Slide 12
2 / 6
Dynamic Element Matching (DEM)
Problem
Component mismatch corrupts current/voltage ratios
Method
Rotate nominally equal elements through switch network
Effect
Mismatch becomes dynamic error, then averages out
Filter Synergy
Same digital filter suppresses DEM ripple + quantization noise
DEM converts static mismatch into average-cancelled error.

## Slide 13
2 / 6
Precision Techniques in Smart Sensors
TECHNIQUE | FIXES | TYPICAL RESULT
Auto-zeroing | Offset, drift | µV-level offset
Chopping | Offset, 1/f noise | nV-level offset
Sigma-Delta ADC | Quantization noise | 20–22 bit resolution
DEM | Component mismatch | ~100 ppm ratio accuracy
Correlated double sampling | Residual offset | Sub-µV performance
Precision is assembled from complementary correction techniques.

## Slide 14
3 / 6
Temperature Sensor: Operating Principle
Sensing Element
Parasitic bipolar transistor available in CMOS
VBE
~−2 mV/°C; useful but process-dependent
ΔVBE
PTAT voltage from 1:p current ratio; process-independent
Challenge
Small signal ~140 µV/K for p=5 → needs low-offset electronics
Temperature sensing turns BJT physics into a precision digital output.

## Slide 15
3 / 6
Temperature Sensor: Circuit Architecture
Core Idea
Sigma-delta modulator converts ΔVBE and VBE into temperature bitstream
No Reference
Temperature is derived without explicit reference voltage
Scale Factor
α = 16 set by sampling capacitor sizing
Accuracy Target
±0.1°C from −55°C to 125°C; offset < 2 µV
Architecture removes reference dependence but demands extreme offset control.

## Slide 16
3 / 6
Temperature Sensor: Error Correction
DEM
Accurate 1:5 bias current ratio using rotating current sources
CDS
Reduces first integrator offset
Chopping
Chops entire modulator; residual offset < 2 µV
Trimming
10-bit current DAC; ~0.01°C resolution
Multiple correction loops synchronize with the main modulator timing.

## Slide 17
3 / 6
Temperature Sensor: Results
Original Design
190 µW and ±0.1°C accuracy across military range
Fast Calibration
Voltage calibration in < 1 second vs. minutes with reference sensor
Two-Step ADC
Binary search followed by sigma-delta conversion
Newer Design
5 µW (≈40× lower power), ±0.15°C accuracy
Smart architecture trades circuit complexity for calibrated precision at low power.

## Slide 18
4 / 6
Wind Sensor: Operating Principle
Solid-State
Measures speed + direction with no moving parts
Thermal Principle
Wind cools a heated object asymmetrically → δT
Flow Encoding
δT magnitude ∝ √speed; δT direction aligns with flow
Packaging
CMOS chip on ceramic disc; housing selects horizontal airflow
Wind is sensed as a controlled thermal imbalance.

## Slide 19
4 / 6
Wind Sensor: Design Approaches
Direct Measurement
4 heaters + 4 thermopiles measure orthogonal δT; µV signals need precision electronics
Cost Problem
Manual trimming + wind-tunnel calibration are slow and expensive
Temperature-Balance Mode
Feedback adjusts heater power to cancel flow-induced δT
Smart Output
Digitize mW-level heater power instead of µV thermopile signals
Smart mode moves the hard measurement from tiny voltage to controllable power.

## Slide 20
4 / 6
Wind Sensor: Circuit Architecture
3 Thermal ΣΔ Loops
North–South δT, East–West δT, constant overheat
Natural Loop Filter
Sensor thermal capacitance acts as modulator loop filter
Compact Electronics
Only clocked comparator per modulator
Microvolt Care
Auto-zeroed comparators handle thermopile signals
The physics of the sensor becomes part of the sigma-delta loop.

## Slide 21
4 / 6
Wind Sensor: Results
Original Test
1–25 m/s wind tunnel range
Accuracy
<4% speed error and <2° direction error
Area
No chip-area increase vs. non-smart version
Newer Design
Constant-power mode: 25 mW (≈16× less), same accuracy
Feedback-based smart sensing improves calibration, power, and robustness.

## Slide 22
5 / 6
Hall Sensor: Operating Principle
Hall Effect
Current-carrying plate in magnetic field → transverse voltage
Tiny Signal
100 V/T sensitivity; Earth field at 1 mA ≈ 5 µV
Offset Problem
Stress, doping, lithography create 5–50 mT offset
Compass Impact
Offset drift becomes time-varying angular error
Hall sensing is useful because it is integrated; difficult because signals are tiny.

## Slide 23
5 / 6
Hall Sensor: Error Correction
Spinning Current
Spatially rotate bias current; time-average output
Orthogonal Coupling
4 Hall plates reduce offset + drift further
Clean Package
Epoxy package avoids ferromagnetic contamination
Nested Chopping
Fast 12.5 kHz + slow ~10 Hz chopping suppress residual offset
Offset cancellation must span device geometry, packaging, and readout electronics.

## Slide 24
5 / 6
Hall Sensor: Results
Offset
4 µT residual offset
Temperature Coeff.
8 nT/K
Drift
<0.25 µT after thermal cycling
Angular Error
<0.5° — best reported CMOS Hall result
Precision interface + packaging turns µV Hall signals into compass-grade sensing.

## Slide 25
6 / 6
Key Takeaways
Smart Sensor
Sensor + interface electronics in one package
Dynamic Correction
Auto-zeroing, chopping, DEM, sigma-delta are essential
Precision Enables
Previously undetectable physical signals become usable
System Design
Optimize sensor, electronics, feedback, calibration, packaging together
Smart sensor design is system optimization, not only sensor selection.

## Slide 26
6 / 6
Looking Ahead
Chapter 2
Calibration and self-calibration techniques
Chapter 3
Precision instrumentation amplifiers
Later Systems
Impedance sensors, gyroscope readout, data processing
Course Link
Apply smart processing / ML to sensor data in later chapters
Next: calibration and precision readout techniques in more depth.